## Slide 1: CSE520 Project Final Demo Real-time Scheduling Evaluation
Yitong Ding, Bojun Li, Ziwei Zhao
11/30/2015

## Slide 2: What we’ve done
Timing API Study
  Compare clock_gettime() and gettimeofday
  Realize rdtsc() in Raspberry Pi
Scheduling Latency Measurement
  Analyze the factors influencing real time latancy
    Idle
    I/O Bound
    CPU Busy

## Slide 3: What we’ve done
Worst Case Execution Time Measurement
  Measure the WCET of benchmark on pi in different system environment
    Idle system
    CPU busy system
    Cache busy system
    I/O busy system

## Slide 4: Timing API

## Slide 5: Why do not choose clock_gettime()

## Slide 6: Comparison
Chart: 10M times’ overhead (in microsecond)
| gettimeofday() | clock_gettime() | direct ticks | pure loop
Overhead | 9465240 | 9770519 | 1240519 | 157375

## Slide 7: We need rdtsc()
Time got from rdtsc() is much more accurate
  No system call
  No math around to fill the structure
However, there is no rdtsc() in Raspberry Pi
Let’s create it ourselves!

## Slide 8: Emulate rdtsc() in Pi
Two ways to realize rdtsc in pi
  Get direct tick
    Read ticks directly from System Timer
  Loadable Kernel Module
    Extend base kernel to add support for rdtsc
    Need assembly language

## Slide 9: Emulate rdtsc() in Pi
The easiest way is to open /dev/mem and map the system clock
Base physical address: 0x20003000
Offset | Name | Description
+0x00 | CS | System Timer Control and Status
+0x04 | CLO | System Timer Counter Lower 32 bits
+0x08 | CHI | System Timer Counter Upper 32 bits
+0x0C | C0 | System Timer Compare 0; corresponds to IRQ line 0
+0x10 | C1 | System Timer Compare 1; corresponds to IRQ line 1
+0x14 | C2 | System Timer Compare 2; corresponds to IRQ line 2
+0x18 | C3 | System Timer Compare 3; corresponds to IRQ line 3

## Slide 10: Emulate rdtsc() in Pi
volatile long long int *timer_api;
timer_api = (long long int *)((char *)TIMER_map + 4);
Example
  Starttime = *timer_api;
  ………
  Endtime = *timer_api;
  Execution time = Starttime – Endtime;

## Slide 11: Comparison
Chart: 10M times’ overhead (in microsecond)
| gettimeofday() | clock_gettime() | direct ticks | pure loop
Overhead | 9465240 | 9770519 | 1240519 | 157375

## Slide 12: Scheduling Latency Measurement

## Slide 13: Scheduling latency
Time until the highest priority task is executed
Evaluate with Cyclictest.
From interrupt to context switch

## Slide 14: Test Loop on Cyclictest
set interval;
clock_gettime(&now);
next = now + interval;
While(!shutdown)
{
  clock_nanosleep((&next));
  clock_gettime((&now));
  diff = now – next;
}
Interval : Period of the task
Suppose interval = 1000 (us)
Tasks released at 0 1000 2000 3000 …(&next)
Tasks executed at 50 1040 2045 3055 …(&now)
Scheduling latency = now – next;
=50 40 45 55
sudo ./cyclictest -p 98 - m -c 0 -i 500 -n -h 500 -q -l 50000 > results.txt
Priority 98
Interval 500us
Stop after 50000 loops

## Slide 15: Scheduling Latency under different scenarios
Idle (no background tasks)
CPU-busy
I/O-busy

## Slide 16: Idle system(no background tasks)
How to emulate an idle system?
No graphic interface
No HDMI
No mouse, no Ethernet cable
Eliminate interrupts
Only a keyboard

## Slide 17
Chart: Scheduling Latency Avg = 40us

## Slide 18: Idle system(no background tasks)
Represents a best-case scenario
Gets baseline results

## Slide 19: CPU-busy system
SQRT: generate an infinite loop of calculation
while (1)
{
a = sqrt(a);
}
Cachebench: cache-intensive workload generator
./sqrt & ./cachebench &./cyclictest

## Slide 20
Chart: Scheduling Latency Avg = 42us

## Slide 21
Chart: CPU-busy vs Idle

## Slide 22: CPU-busy system
Expected to have worsened Latency than an idle system
more cache miss (cache-busy)
more context switch (CPU-busy)

## Slide 23: I/O busy system
Hackbench&Netperf
hackbench: causing frequent system calls and scheduler invocations
netperf: generate network data transfer
generate lots of I/O interrupts

## Slide 24
Chart: Scheduling Latency Avg = 77us

## Slide 25
Chart: Scheduling Latency

## Slide 26: I/O busy system
Scheduling Latency is severly affected by I/O tasks.

## Slide 27: Multi-core scheduling latency research
Raspberry pi 2
quad-core ARM Cortex-A7 CPU
1GB RAM

## Slide 28: Multi-core scheduling latency research
Taskset : set or retrieve the CPU affinity
taskset -c X - p 12345
Set the processor affinity of process 12345 to processor #X
CPU0: Avg:18 Max:599
CPU1: Avg:17 Max:56
CPU2: Avg:17 Max:40
CPU3: Avg:17 Max:38

## Slide 29: Multi-core scheduling latency research
/proc/interrupts
CPU0 CPU1 CPU2 CPU3
16: 0 0 0 0
20: 1410 0 0 0
32: 4390679 0 0 0
49: 0 0 0 0
50: 0 0 0 0
65: 25 0 0 0
66: 2 0 0 0
75: 1 0 0 0
77: 126 0 0 0
83: 5 0 0 0
84: 11390 0 0 0
96: 0 0 0 0
Most of the interrupts go to CPU0

## Slide 30: WCET Measurement

## Slide 31: Benchmark
Sqrt() – Forces on floating point calculation
for (i = 0; i < 2000; i++)
temp = sqrt((double)i*i);

## Slide 32: Test configuration
At high priority (98)
With period of 100 ms
Run for 10 second
Gather 100 samples
Repeat for 3 times

## Slide 33: Test environment
Idle system
CPU busy system
generated by infinite loop of sqrt().
Cache busy system
generated by cachebench.
I/O busy system
generated by netperf.

## Slide 34: Sqrt() in idle system

## Slide 35: Possible interference
1. init
2. ifplugd
3. ntpd
4. rcu_preempt
5. kworker
6. ksoftirpd
7. etc.
Notes: 1.In Unix-based computer operating systems, init (short for initialization) is the first process started during booting of the computer system. Init is a daemon process that continues running until the system is shut down.
2. ifplugd is a daemon which will automatically configure your ethernet device when a cable is plugged in and automatically unconfigure it if the cable is pulled.
3. The ntpd program is an operating system daemon which sets and maintains the system time of day in synchronism with Internet standard time servers.
4. RCU is a synchronization mechanism that is optimized for read-mostly situations. The basic idea behind RCU is to split updates into "removal" and "reclamation" phases.
5. "kworker" is a placeholder process for kernel worker threads, which perform most of the actual processing for the kernel, especially in cases where there are interrupts, timers, I/O, etc. These typically correspond to the vast majority of any allocated "system" time to running processes. It is not something that can be safely removed from the system in any way
6. ksoftirqd is a per-cpu kernel thread that runs when the machine is under heavy soft-interrupt load. Soft interrupts are normally serviced on return from a hard interrupt, but it's possible for soft interrupts to be triggered more quickly than they can be serviced. If a soft interrupt is triggered for a second time while soft interrupts are being handled, the ksoftirq daemon is triggered to handle the soft interrupts in process context. If ksoftirqd is taking more than a tiny percentage of CPU time, this indicates the machine is under heavy soft interrupt load.

## Slide 36: Sqrt() in cpu busy system

## Slide 37: Sqrt() in cache busy system

## Slide 38: Sqrt() in I/O busy system

## Slide 39: Summery for sqrt()
Time in us | Idle | CPU Busy | Cache Busy | I/O Busy
Average | 492 | 486 | 491 | 532
WCET(99%) | 535 | 542 | 545 | 617
WCET | 543 | 551 | 683 | 1013